## Slide 1: Algorithm Flow for Road Sign Detection System and Analysis
Final Year Project By:
Nishad Harsulkar
Saurabh Autade
Sujal Koli
Academic Year 2024-25 A Project Presentation on
Guided By
Prof. Sarika N. Patil
Department of Electronics and Telecommunication Engineering,
Nutan Maharashtra Institute of Engineering and Technology, Talegaon Dabhade, Maharashtra 410507
Savitribai Phule Pune University, Pune.

## Slide 2: Flow of the System
Input from Camera
Input from Accelerometer
Input from GPS
Beep the Alarm
Data Comparison
Detection and Recognition
If No Rule Break
If Rule Break
Sensor Fusion

## Slide 3: Considerations:
As it can be seen from the flow of the system, we have 3 sensors responsible for producing data.
Camera – To detect signs ; Accelerometer – To get real-time speed;
GPS – To get real time coordinates.
Out of these, to set hierarchy plus considering the basic logic of our system, Camera input is of top priority. Without it there is no use of real time speed and if there's no comparison of Detected sign and speed then there's also no use of GPS coordinates. So Camera  Accelerometer  GPS.
Overall the output of system is directly dependent on the detection, which should also be accurate and with minimal latency.

## Slide 4
Defining the minimal latency, a standard camera operates at 30 FPS i.e. 33 ms for 1 image. A standard accelerometer gives speed at 5Hz i.e. 200 ms for 1 sample. A standard GPS gives updates at 1Hz i.e. 1000 ms for 1 sample.
This will create data mismatch and wont be ideal for working of the system. For that let us set some limitations.
Consider we have 3 functions Camera, Speed and GPS which runs parallelly and publish data according to their respective frequency.
Now, suppose we expect output from each function for every 50 ms. In this case Camera can give new updated output for every iteration (0,50,100,150) but Speed and GPS will have problem here. For that we can take their previous outputs.
At 0ms if Speed was 10 km/h, we will get next Speed update at 200ms. So till that for iterations of 50, 100 and 150 we can consider speed as 10 km/h. This assumption can be backed by the fact that there is not drastic change in speed of a vehicle in 200 ms. If there it can be notes after 200 ms that is 1/5th of 1 second.
Camera
33 ms
Speed
200ms
GPS
1000 ms

## Slide 5
At 0ms if GPS was [11 Lat ,34 Long], we will get next GPS update at 1000ms. So till that for iterations of 50, 100, 150 and so on till 1000 we can consider GPS as [11 Lat,34 Long]. This assumption can be backed by the fact that there is a drastic change of location of vehicle which is at high speed for every 1000 ms or 1 second, but if its previous location is considered and our motive for taking GPS coordinates is taken into account, then rule break has happened near to this noted location can be proved.
But delays in Camera detection cannot be tolerated as it is crucial for next comparisons. Changes in scenario can happen at very few milli seconds (10-30 ms) so detecting them is important.

## Slide 6: Solutions
Check for GitHub repos related to the problem
The problem of Red light being detected from far can be also solved by knowing how Smart Cameras at traffic signal detect if vehicle has stopped at signal or not.